## Slide 1: Permanent 3D laser scanning system for an active landslide in Gresten (Austria) Canli, E.1, Höfle, B.2, Hämmerle, M.2, Thiebes, B.1,3, Glade, T.1 1 University of Vienna (ekrem.canli@univie.ac.at), 2 Heidelberg University, 3 EURAC research
1. Idea
3. Workflow
2. Installation
4. First Results
Navigation
Click buttons for more information
Enlarge pictures by clicking on it
Study site

## Slide 2: Permanent 3D laser scanning system for an active landslide in Gresten (Austria) Canli, E.1, Höfle, B.2, Hämmerle, M.2, Thiebes, B.1,3, Glade, T.1 1 University of Vienna (ekrem.canli@univie.ac.at), 2 Heidelberg University, 3 EURAC research
[Idea]
Terrestrial laser scanners (TLS) widely used for high spatial resolution data acquisition (landslides, rockfalls, debris flows, etc.)
Many advantages:
  High spatial sampling density of XYZ-measurements (compared to low data density surface monitoring techniques; e.g. GNSS or total station)
  mm accuracy/precision of measurement & cm accuracy of final DEM
  Capability of highly dense area-wide scanning that enables to look through vegetation
Main constraints: low temporal resolution (labor costs, time requirements for field campaigns) --> only episodical repetition measurements (e.g. once per year)
To gain an increased scientific understanding of a process, we present a novel permanent 3D monitoring setup to increase the temporal resolution of TLS measurements (pTLS)
1. Idea
3. Workflow
2. Installation
4. First Results
Navigation
Click buttons for more information
Enlarge pictures by clicking on it
Study site
Notes: BENNI: pTLS steht für „permanent TLS“…das vllt explizit erwähnen – wär cool, wenn sich dieser Begriff etablieren könnte

## Slide 3: Permanent 3D laser scanning system for an active landslide in Gresten (Austria) Canli, E.1, Höfle, B.2, Hämmerle, M.2, Thiebes, B.1,3, Glade, T.1 1 University of Vienna (ekrem.canli@univie.ac.at), 2 Heidelberg University, 3 EURAC research
[Installation]
Optech ILRIS-3D scanner mounted on massive surveying pillar
Encased in custom made protective box
  Permanent connection to power supply and internet
  Isolated; cooler/heater
  Optical glass; prevents reflections, high (near) infrared transmissivity
Field of view (FoV) from the fixed scanner position covers most of the active landslide surface (with a maximum distance of ca. 300 m)
Navigation
Click buttons for more information
Enlarge pictures by clicking on it
1. Idea
3. Workflow
2. Installation
4. First Results
Study site

## Slide 4: Permanent 3D laser scanning system for an active landslide in Gresten (Austria) Canli, E.1, Höfle, B.2, Hämmerle, M.2, Thiebes, B.1,3, Glade, T.1 1 University of Vienna (ekrem.canli@univie.ac.at), 2 Heidelberg University, 3 EURAC research
[Workflow]
pTLS autonomously operated by time switch and scripts
Performs 1 scan/day; data transmission via internet to server in Vienna
Each scan contains XYZ (+intensity) ASCII file, coloured picture, and scan metadata
Single independent scan with a Riegl VZ-6000 acts as reference measurement (global coordinate system GCS, i.e. UTM/WGS84)
pTLS scans (scanner own coord. system) are automatically transformed into the GCS with 3D-transformation using matching of corresponding point pair coordinates of tie reflectors
Derivation of Digital Elevation Models (DEM): Digital Terrain Model (DTM), Digital Surface Model (DSM)
Calculation of Difference Models (raster/point cloud): daily, weekly, annually, and for selected time intervals
Navigation
Click buttons for more information
Enlarge pictures by clicking on it
1. Idea
3. Workflow
2. Installation
4. First Results
Study site
XYZ + Intensity + RGB
Point Clouds
Notes: [BENNI: point pairs sind so kleine Reflektorscheiben außerhalb der Rutschung, die mit dem Tachy eingemessen wurden)

## Slide 5: Permanent 3D laser scanning system for an active landslide in Gresten (Austria) Canli, E.1, Höfle, B.2, Hämmerle, M.2, Thiebes, B.1,3, Glade, T.1 1 University of Vienna (ekrem.canli@univie.ac.at), 2 Heidelberg University, 3 EURAC research
[First Results]
48 daily datasets already captured with approx. 1.3 billion points in total
Next steps
Implementation of web tool to derive descriptive statistics and time series plots of changes in near-realtime (i.e. before next scan)
Improvement of terrain classification by including point cloud time series (not just taking one point cloud for classification)
Navigation
Click buttons for more information
Enlarge pictures by clicking on it
1. Idea
3. Workflow
2. Installation
4. First Results
Study site
Intensity-based detection of tie reflectors for georeferencing
Terrain filtering (DTM)
Cloud-to-Cloud Difference (M3C2)

## Slide 6
[close]

## Slide 7
[close]

## Slide 8: Permanent 3D laser scanning system for an active landslide in Gresten (Austria) Canli, E.1, Höfle, B.2, Hämmerle, M.2, Thiebes, B.1,3, Glade, T.1 1 University of Vienna (ekrem.canli@univie.ac.at), 2 Heidelberg University, 3 EURAC research
[Study site]
Salcher landslide in Gresten (Lower Austria)
Navigation
Click buttons for more information
Enlarge pictures by clicking on it
1. Idea
3. Workflow
2. Installation
4. First Results
Slow moving, mainly translational landslide
Situated in the Austrian Pre-Alps (transition zone between Flyschzone and Klippenbelt)
Varying movement rates; up to 20 cm/a
Initial movements reported in July 1975
also: EGU2015-223
Canli et al.: „Multi-parameter monitoring of a slow moving landslide in Gresten (Austria)“
Session NH3.4, room G1, Wed., 15. Apr 2015, 08:30
pTLS pos.

## Slide 9
[close]

## Slide 10
[close]

## Slide 11
[close]
pTLS pos.